## Slide 1: Spline
Hull design

## Slide 2: SolidWorks Sketch Commands
Drawing tools
Modifying tools
Trim and Extend
Dimensioning tool
Checks sketch for problems
Project entities
Offset
Mirror
Rectangular and Polar (circular) array
Constraints
Spline

## Slide 3
Bezier Curve – tangent to the first and last segment of the polygon
Splines
Cubic spline – fits a smooth curve thru the points
Control points

## Slide 4: B-Spline
Same as the Bezier curve but with Local control

## Slide 5: Spline Command in SW
A smooth curve is fitted through selected points (on flat surface)
Active only in 3D sketch mode on curved surfaces

## Slide 6: Spline Command in SW
SolidWorks generates a smooth curve passing through all data points. The shape can be manipulated by control points and tangent vectors.
Point #2 modified from (1,1) to (1,2)
X & Y coordinates of the point, Y changed from 1 to 2.
Data point #2
Point #
Tangent Driving box is checked off

## Slide 7: Spline Command in SW
The spline shape can be modified by manipulating the Tangent vector for each point.
Data point #3 is selected
Size (weight)
angle

## Slide 8: Style Spline
Style Spline
Spline
Modified
Better control with Style Spline

## Slide 9: Spline on a curved surface
Select the curved surface to draw
Select the 3D Sketch option
Select the Spline on Surface option

## Slide 10
Sketch the curve
Exit the sketch
Select Extrude Cut option , choose the spline curve and the direction for extrusion
Direction

## Slide 11
Select body to keep

## Slide 12: Curves defined by equations
Mathematical Equation
x + sin(x)

## Slide 13: Clicker Question
When using Spline in SW, points are selected on the screen first. Which statement is true?
A smooth curve is fitted between the points selected
B) A smooth curve is fitted through the points
selected
C) A tangent curve, to the start and end polygons,
is generated
D) A polygon is created by connecting the points

## Slide 14: Conic Curves

## Slide 15
Creating a conic in SolidWorks is very simple. It builds much like a 3-point-arc, but instead of adjusting a radius value, it adjusts a parameter called Rho (ρ). If you imagine the conic as a rounded corner, then Rho is the ratio of the distance of the peak of the rounded corner to the sharp corner (D1/D2). This gives us an intuitive way to adjust the curvature of the conic without having to delve into which type of conic section it is, or what its mathematical eccentricity is.

## Slide 16: SolidWorks Conic Command
2 – select the Apex
1 – select the two end points start
3 – Select the Rho () value

## Slide 18: SolidWorks Sketch Commands
Importing an image into the sketch environment
Use Spline to trace the curve

## Slide 19: Projecting Entities onto a Sketch plane
Projected entities

## Slide 20: Constraints
Select Add Relations
Select line
Select Vertical

## Slide 21: Constraints
Select two entities (lines)
Select Collinear
Tangent constraint

## Slide 22: Constraints
Two curved entities
Two straight entities
Curved & straight entities

## Slide 23: Repair Sketch Option