## Slide 1: Manufacturing Process - Extrusion
Parts have a uniform (constant) cross section

## Slide 2: Extrusion
Material (billet), hot or cold, is either pushed or pulled through a die. The long piece can be cut to a desired thickness

## Slide 3: Extrude Command in SolidWorks
Adds material
Removes material

## Slide 4: Extrusion
Create a 2D sketch
Select the sketch
Preview of the solid, there is a problem with the sketch if the preview does not appear, most likely the sketch is not continuous
Select Extruded Boss/Base
Choose Blind and enter the thickness and accept

## Slide 5: Extrusion
Click to change the direction of the extrusion
Click on the arrow and drag to change the thickness using the scale on the screen
On screen scale

## Slide 6: Extrusion
Two directions could be used for extrusion: direction 1 (15 mm), direction 2 (5 mm)
thickness15 mm
thickness5 mm

## Slide 7: Extrusion

## Slide 8: Extrusion
The part can be hollowed out by selecting the Thin Feature option and assigning a value for the wall thickness
5 mm wall thickness
Copper material rendered

## Slide 9: Extrusion
To taper the extrusion: select the taper option and assign the desired taper angle in degrees, 15 degrees.
No taper

## Slide 10: Revolve Command
Select the revolve command, choose the axis of rotation and the amount of rotation in degrees. The axis of revolution could be any line in the sketch.
Axis of rotation
Sketch
360 deg. revolution
180 deg. revolution

## Slide 11: Revolve
The part can be hollowed out by selecting the Thin Feature option and assigning a value for the wall thickness
Rendered model