## Slide 1
Product list is due next week Friday Sept. 25 by 11:59 pm. Upload your list to Canvas.
You are asked to come up with 5 ideas for either new products or modification of an existing product. The list should only be ideas that can be built physically
√
√
√
X
X
Not enough explanation

## Slide 3
Circular Profile – automatically uses a circle as the Profile.
Sweep Command in SW

## Slide 4: Sweep Command in SW
Path
Profile
Sweep needs a profile (section) and a path (guide)
The guide must intersect the section

## Slide 5
Sweep using a profile, path and Follow Path option
Profile (Sketch 5)
Path (Sketch 7)

## Slide 6
Follow Path
Sweep Command in SW
Sweeps using different Options
Keep normal constant
Twisted

## Slide 7
Guide curve 1
Profile
Path
Sweep Command in SW
Sweep using a profile, path and one guide
1
1
2
2
3
3
Profile
Sketch11
Sketch10

## Slide 8: Sweep Command in SW
Sweep using a profile, path and two guides
Profile 1
Path 1
Guide Curve 1
Guide Curve 2

## Slide 9
Loft Command in SW
Loft command creates a surface or a solid by sweeping and blending using two or more different profiles.
Profile 1
Profile 2
Guide curve
Draw the guide curve first then create two reference planes at the ends of the guide curve perpendicular to the curve

## Slide 10
Loft without any guide curve

## Slide 11
Loft using a guide curve

## Slide 12
None or normal to Profile with 0 angle at both ends
End Constraints
Normal to Profile with 0 angle at top but 20o at the bottom

## Slide 13: Loft Command in SW
Profile normal to the plane at one end
Profile normal to the plane at both ends

## Slide 14: Loft Command in SW
Loft using a single Guide Curve.
Profile
Profile
Guide, 3D sketch

## Slide 15: Loft Command in SW
Loft using 4 Guide Curves.
Guide 1
Guide 2
Guide 4
Guide 3
Guides 1,2
Guides 1,2,3
Guides 1,2,3,4

## Slide 16: Loft Command in SW
Merging a Loft with a feature

## Slide 17: Clicker Question 1
For the Loft command to work, which statement is true?
One profile and one path curve (guide) is required
B) One profile and two path curves (guide) are required
C) At least two profiles
D) Multiple profiles and guide curves could be used
E) C and D

## Slide 19
10 spline sketches on 10 planes .3 inches apart

## Slide 21: Example

## Slide 26
Knife handle

## Slide 27
Knife blade
Hand and wrist

## Slide 28: Clicker Question 2
Which of the following statement(s) is true?
Sweep requires one profile and two paths
B) Sweep requires one profile and one path
C) Loft requires at least two profiles and one path
D) Guide curves could be used in both Sweep and Loft
E) B, C and D