## Slide 1: Construction of Reference Planes

## Slide 2
Principal planes (front, top, right side)
Any flat surface of the object could be used as a sketch plane

## Slide 3
Creating reference (Datum) planes
Right click in the menu area and select Reference Geometry
Reference plane

## Slide 4: Reference Features
The reasons you may need Reference features
To locate a sketch for a new feature where a model surface is not available; construct a reference plane to sketch.
To establish a plane or an edge for dimensioning; construct reference plane or reference axis.
To provide a point for rotating or an axis for revolving features or patterns; construct reference point or reference axis
To establish an intermediate position that is required to define other reference plane; construct a reference plane

## Slide 5: Constructing Reference Planes
Selecting three points
Selecting two parallel lines
Selecting two intersecting lines
Selecting a point and a line
A plane can be uniquely defined by:

## Slide 6: Reference Plane
Reference plane is a rectangular plane that is tied to the model parametrically and is infinitely large. There is no limit on the number of reference planes and they can be used to create new sketches for feature operations.

## Slide 7
Select three points to create a reference plane
1st point
2nd point
A unique plane is passing through the three points
3rd point
Green indicates that the plane is fully defined.

## Slide 8
Specify two lines to construct the plane
Line (Edge) 1
Line (Edge) 2

## Slide 9
Parallel plane with a specified offset (20 mm)
Select a face and specify the offset
Perpendicular to a plane and thru a selected line

## Slide 10
Reference plane at a specified angle with respect to another plane
Reference plane tangent to a curve at a specified point

## Slide 11
A
Cut an object at a desired location (point A) with a specified angle
Select the top plane as a sketch plane and locate point A. Pass a line thru point A
Create a reference plane (cutting plane) by selecting the top surface and the line passing thru A
Top surface
Line thru A
Cutting plane
A

## Slide 12
Select cutting tool (plane) and cut the part (cylinder). Choose the section to erase.