## Slide 1: Robot Electronics

## Slide 2
R1 = 68.1k  R2 = 249k 
R3 = 2.8k 
R4 = 10k 
R5 = 10k 
R6 = 100k 
R7 = 8.06k 
R15 = 1k  R16 = 100 
R17 = 2.8k 
R18 = 2.8k 
R19 = 2.8k 
R20 = 2.8k 
R8 = 5.11k  R9 = 82.5k 
R10 = 10k 
R11 = 10k 
R12 = 10k 
R13 = 10k 
R14 = 10k 
C1 = 10v 680 F C2 = 10v 47 F
C3 = 474, .47 F C4 = 10v 47 F
C7 = 102, 1 nF
C8 = 103, .01 F
C11 = 102, 1 nF
C12 = 103, .01 F
C13 = 104, .1 F
C14 = 104, .1 F
C15 = 104, .1 F
C16 = 104, .1 F
C17 = 104, .1 F
Q1 = 2N7000 Q2 = 2N7000
Q3 = 2N3906
U1 = CD4051, 16-pin U2 = CD4052, 16-pin
U3 = MC33204P, 14-pin
U4 = CD4520, 16-pin
Resistors
Capacitors
Transistors
LEDs
Integrated Circuits
Infrared Detectors
Polarized (+,-)
Non-Polarized
8 – white color
5 – red
color
Robot Project - The IR board
ky
Short lead
Long lead

## Slide 3
Resistors are passive elements that oppose/restrict the flow of current.
A voltage is developed across its terminal, proportional to the current through the resistor.
V = IR
Resistors
Component ID | Value | Marking
R15 | 1k Ω | 1k 1%
R4,5,10,11,12,13,14 | 10k Ω | 10k 1%
R6 | 100k Ω | 100k 1%
R16 | 100Ω | 100Ω 1%
R3, 17,18,19,20 | 2.8k Ω | 2.8k 1%
R2 | 249k Ω | 249k 1%
R8 | 5.11k Ω | 5.11k 1%
R1 | 68.1k Ω | 68.1k 1%
R7 | 8.06k Ω | 8.06k 1%
R9 | 82.5k Ω | 82.5k 1%
Resistor ID and values for the IRB
Units: Ohms (Ω)
Variable resistor (potentiometer)
Constant resistor

## Slide 4
Capacitors
Store energy and release it later (small battery) (store energy and release it later. )
are made of two parallel conductors separated by a dielectric.
are used for filtering, tuning, separating signals , etc.
The ability of a capacitor to store charge is called “Capacitance”
C = Q/V (amount of charge stored/applied voltage)
The unit of capacitance is the Farad. Commonly used capacitances are much smaller than 1 Farad, micro-Farads (10-6 Farad, μF),
nano-Farads (10-9 Farad, nF), pico-Farads (10-12 Farad, pF).

## Slide 5
Component ID | Value | marking | Remark
C2, 4 | 47μF | 47μF 10v | polarized
C1 | 680uF | 10v 480μF | polarized
C7, C11 | 1nF | 102 | Not polarized
C8, C12 | .01μF | 103 | Not polarized
C13, 14, 15, 16, 17 | 0.1μF | 104 | Not polarized
C3 | 0.47μF | 474 | Not polarized
Capacitor ID numbers, capacitances, and markings on the capacitors

## Slide 6
Symbol for the NPN Transistor
Symbol for the PNP Transistor
Transistors are commonly used for signal amplification, switching, voltage regulation, etc.
base
emitter
collector
Transistors
Transistor ID | Transistor type | Marking
Q1, Q2 | 2N7000 | 2N7000
Q3 | 2N3906 | 2N3906
Transistor ID numbers, types, and markings on the transistors.

## Slide 7
Diodes are semiconductor devices that allow
current in only one direction
Fuses are devices that protect the circuit from overload.

## Slide 8
LEDs- Light Emitting Diodes:
A special kind of diode: They allow current to flow in one direction.
The LED will light up when the proper amount of current passes through.
1-3
4
5

## Slide 9
Infrared Detectors
The appearance of these infrared photo detectors and the internal structure is similar to that of an LED.
The infrared photo detector has a focal direction, and the detection angle is about 15°. (8x15=120˚)
This small detection angle allows the controller to tell the direction where the infrared light comes from.

## Slide 10
Sockets for Integrated Circuits
Must be soldered in position before the ICs are inserted
Component ID | Type | Marking
U3 | DIP14 socket | 14-pin
U1, 2, 4 | DIP16 socket | 16-pin
IC socket ID numbers and type.

## Slide 11
Tuning CKT
Amplifier
Selector
Counter
Integrated Circuits
Orientation
ID | Parts number | Function
U1 | CD4051 | 8 to 1 multiplexer
U2 | CD4052 | Due 4 to 1 multiplexer
U3 | MC33204P | Rail-to-Rail Op Amp
U4 | CD4520 | Counter
IC parts number and function.

## Slide 12
There are two connectors on the board – J1 and J2. J1 is a 10-pin ribbon cable connector. J2 is a 3-pin stick connector. J1 should be placed according to Figure 12. J2 can be placed in either orientation but the shorter pin side should be placed into the holes. You will see a place on the circuit board labeled for J3. For this project, J3 is not used.
  Connectors