## Slide 1: SolidWorks
Select File

## Slide 2: Part Modeling
Select File  New  Part (already selected)

## Slide 3: Sketcher Layout

## Slide 4
Select Sketch and choose Sketch (2D)

## Slide 5: Start Sketching
Principle planes
Part manager, keeps track of all your work (modeling)
Sketch tools

## Slide 6: Sketching
Draw using the sketch tools
Make sure the new line snaps to the end of the previous line (indicated by the large circle), do not guess the location
Origin (0,0)
Feedback from sketcher, vertical and horizontal
Midpoint
Tangent

## Slide 7: Assigning Units
To assign units, select Tools and then Options
Select Document Properties, Units and choose the Unit system desired

## Slide 8: Dimensioning
To dimension, select Smart Dimension, click on the line, drag to a desired location, click again and enter value
To edit dimension, double click the value and enter the new value

## Slide 9: Making a Solid from the Sketch
Right click for other option like dimensioning
Exit sketch

## Slide 10: Features
Select Features

## Slide 11
Select thickness
Extrusion, select Blind and assign a thickness

## Slide 12
Thin feature in Extrusion
Thickness
Hollowing out as you Extrude

## Slide 13
Revolve, select axis of rotation and amount of rotation
Select a line to revolve about
Select the Revolve option

## Slide 14
To make a hole at the top, select Sketch, select top surface and draw a circle

## Slide 15
Select Extruded Cut option

## Slide 16: Features
Feature Menu
Solid making commands, a two dimensional sketch is needed
Extrude – create (unite or join)
Extrude – cut (subtract)
Revolve– create (unite or join)
Revolve – cut (subtract)
Sweep – create (unite or join)
Sweep – cut (subtract)
Loft (sweep and blend)– create (unite or join)
Loft (sweep and blend – cut (subtract)
Applied features, no need for a sketch
Fillet (round edges)
Pattern (circular and linear)

## Slide 17: Display Menu
Wireframe
Shaded view
Shaded view with edges shown
Solid with hidden lines shown
Solid not shaded
Zooms the model to fit the screen
Zooms to a specified area by opening a window
Displays the previous view
Scrolls the view, Pan
Display style
To rotate the model on the screen: hold the middle mouse button down and move the mouse