## Slide 1: Vex Ultrasonic Sensor (US) Interfacing and Programming

## Slide 2: Ultrasonic Sensors
Generally have a transmitter and receiver.
Transmits a high-frequency sound.
Waits to receive echo.
Calculates distance based on time it took to receive the echo.
Round-Trip Distance
One-Way Distance
d = distance, v = speed of sound, t = time to receive echo
2
d = (v)(t)
d = (v)(t)/2

## Slide 3: The Vex Ultrasonic Sensor
INPUT
Sends ultrasonic wave
Connect to digital output of the controller
OUTPUT
Receives the echo
Connect to the input of the controller
The labeling is a bit counter-intuitive!
3

## Slide 4: Connecting the sensor to the controller

## Slide 5: Ultrasonic Sensor Programming
Sensor connected to input port 5
Sensor connected to output port 6 through which it receives digital control signals from the controller.
The following statement starts an ultrasonic sensor i.e., the sensor starts sending and recording the sound signals.
StartUltrasonic ( 5, 6 ) ;
Select start

## Slide 6: Ultrasonic Sensor
Variable into which the translated value is stored
Input to Ultrasonic port #5
The sensor is connected to output port # 6 on the controller
The following statement is used to read a value from the sensor
Range = GetUltrasonic ( 5 , 6 );
Select Get option
Define variable Range

## Slide 7
Cortex Controller
Digital ports taken by the IRB
Change port 6 from input to output by clicking on the circle
Select Config to Change input port #6 to an output port

## Slide 8
Input to Ultrasonic sensor connected to output port 6 on controller
Output from Ultrasonic sensor connected to input port 5 on controller
Checking if the obstacle is near or far