## Slide 1: Bit Masking
To access or affect only the bits we want, we need to construct a byte with bits set in the locations of interest
  This byte is called a ‘bit mask’
Use the bit mask with the appropriate bit-wise operator to get the desired result:
  To set bits: bit-wise OR ( | ) with the bit mask
  To clear bits: bit-wise AND ( & ) with the negated bit mask

## Slide 2: Bit Masking Example 1
Set bits 3, 5, and 7 in DDRD (make pins to be OUTPUTS) without affecting the other bits (port-style):
  recall: DDRD = 0b10101000; but this would make pins 6, 4, 2, 1, and 0 to be INPUTS, which might not be what we want
  Instead:
    Construct a bit mask with 1s in bit positions 3, 5, and 7 and 0s everywhere else
    Bit-wise OR with DDRD and assign back to DDRD

## Slide 3: Bit-Wise OR and AND
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Bit-wise OR (X | Y)
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Bit-wise AND (X & Y)

## Slide 4: Bit Masking Example 1, cont. (setting bits 3, 5, and 7 in DDRD)
Bit mask with bits set in positions 3, 5, and 7:
Many ways to do this:
  Write directly in binary: 0b10101000
  Write in hex or decimal: 0xA8 or 168
  Left-shift with OR: (1<<7 | 1<<5 | 1<<3)
Bit-wise OR with DDRD and assign back
  DDRD = DDRD | (bit mask from step 1)
  DDRD = DDRD | (1<<7 | 1<<5 | 1<<3);
  DDRD | = (1<<7 | 1<<5 | 1<<3); // ‘shortcut’

## Slide 5: Bit Masking Example 2
Your turn: turn on the pull-up resistors for pins 1, 4, and 6 (assuming that they are already made to be INPUTS) without affecting the other pins
  PORTD | = ( (1<<1) | (1<<4) | (1<<6) );
Notes: PORTD | = ( (1<<1) | (1<<4) | (1<<6) );

## Slide 6: Bit Masking Example 3
Turn off the pull-up resistors for pins 1, 4, and 6 without affecting the other pins
  Need to clear bits 1, 4, and 6 in PORTD register without affecting the other bits
Construct a bit mask with 1s in bit positions 1, 4, and 6
Bit-wise AND PORTD with the negated bit mask and re-assign to PORTD

## Slide 7: Negate Bits
Negate bits with the ~ operator
  ~ 01010010  10101101

## Slide 8: Bit Masking Example 3, cont. (clear bits 1, 4, and 6 in PORTD)
Your turn:
  Construct a bit mask with 1s in bit positions 1, 4, and 6
  Bit-wise AND with the negated bit mask:
    byte bit_mask = (1<<6) | (1<<4) | (1<<1);
    PORTD &= ~bit_mask;

## Slide 9: Summary So Far
To ‘set’ bits port-style:
  Construct a bit-mask with bits in the location(s) of interest
  Execute bit-wise OR ( | )with assignment back to the register of interest
To ‘clear’ bits port-style:
  Construct a bit-mask with bits in the location(s) of interest
  Execute bit-wise AND ( & ) (with the negated bit mask) with assignment back to the register of interest

## Slide 10: Determining if a bit is set or cleared
Arduino style (easy!): if( digitalRead(pin) )
Port-style:
  Construct a bit mask with bits in the locations of interest
  Bit-wise AND the PINx register with the bit mask
  Test the result
Example:
  Is a SPST switch on pin D1 closed?

## Slide 11: Example for determining if a bit is set or cleared
  Suppose a SPST switch between pin D1 and ground
    Take action if it is closed
Arduino style (easy!)
  if ( digitalRead(pin_D1) == LOW ) { do stuff; }
Port-style:
  Construct the bit mask:
  byte bit_mask = ( 1<<1 );
  Bit-wise AND the bit mask with the PIND register
  Test the result
  if ( (PIND & bit_mask) == bit_mask ) { do stuff; }