## Slide 1: Digital-to-Analog & Analog-to-Digital Conversion
BJ Furman
21APR2016

## Slide 2: DAC and ADC
Digital-to-Analog Conversion (DAC)
  Converts a binary value to a scaled ‘analog’ voltage
  Used for controlling systems that require an analog input.
    DC servo motor
    Resistive heater, etc.
Analog-to-Digital Conversion (ADC)
  Converts a continuous analog voltage into discrete binary values
    Used to translate continuous physical phenomena into a language the computer understands.

## Slide 3: R-2R Ladder DAC (4-bit)
2R
2R
R
2R
R
2R
R
+
-
R
Vref
Vout
MSB
LSB
2R
bit 3
bit 2
bit 1
bit 0
a
b
c
d
“switches”
What are the voltages at nodes a - d?
Develop a general expression for Vout
Use the general expression to determine Vout if the switch associated with bit 2 is connected to the amplifier.
Notes: Think about the configuration of the amplifier. What is it? (summing amp). What voltages (at nodes a – d) are being summed? To see the pattern, start with the chunk of the circuit from node c toward the right. What is the voltage at node d? Well, the two resistors that connect at node d are each 2R. At the other end of these resistors is either real ground or ‘virtual ground’. We can view these two resistors as an equivalent resistor of value R (the parallel combination of two Rs). Thus, the combination of the resistor between c and d (R) and the equivalent R connected to d forms a voltage divider. The voltage at d is Vc/2. If we move up the ladder (to the left), we can perform a similar analysis for the voltage at node b. We will find that Vb = Va/2. Summarizing:
Va = Vref
Vb = Va/2
Vc = Vb/2 = Va/4
Vd = Vc/2 = Vb/4 = Va/8
If any one of the ‘switches’ is thrown so that it connects to the inverting terminal of the amplifier, (bitn=1) what we have is
Vout = -(R/2R)Vref [ bit3*Va + bit2*Vb + bit1*Vc + bit0*Vd ]
Vout = -Vref[ bit3/2 + bit2/4 + bit1/8 + bit0/16 ]
Thus, the basic resolution of the DAC is 1/(2^n), where n is the number of bits (switches) that the DAC has.

## Slide 4: Digital to Analog Converter (DAC)
R-2R Ladder DAC is widely used
  It’s a programmable summing amplifier
    The smallest change in voltage (the ‘resolution’) that can be output by the DAC is determined by the number of bits:
      Resolution = Vref / 2N , where N is the number of bits
        Given Vref = 5 V, and a 10-bit DAC, what is the smallest change in voltage that the DAC can output?
Notes: 5 V/ 210= 5 V/1024 = 0.0049 V  4.9 mV

## Slide 5: Successive Approximation ADC
http://upload.wikimedia.org/wikipedia/en/6/61/SA_ADC_block_diagram.png

## Slide 6: A successive approximation ADC is like a beam balance
https://i.ytimg.com/vi/l-SLEqOT5l8/maxresdefault.jpg
http://www.sciencelabsupplies.com/g
1
2
3

## Slide 7: A successive approximation ADC is like a beam balance
Stiffler, A.K. (1992). Design with microprocessors for mechanical engineers. McGraw-Hill, NY.

## Slide 8: 8-bit Successive Approximation ADC
From Necsulescu, D., (2002). Mechatronics, Prentice-Hall, New Jersey.

## Slide 9: ATmega ADC system
Clock input of 50 kHz to 200 kHz for maximum resolution
Voltage reference (AVCC) (input voltage range) is selectable
  Default is to Vcc=5 V
  1.1 V
  Something else on AREF
    Be careful!
  See http://arduino.cc/en/Reference/AnalogReference
Notes: Analog measurements are all ‘single-ended’, i.e., voltages are measured with respect to GND. Other microcontrollers (ex. ATmega32) also has the capability to measure differential voltages.

## Slide 10: It takes time to complete an ADC conversion
First takes 25 ADC clock cycles
Subsequent, 13 ADC clock cycles
Source: ATmega328 data sheet, p. 251