## Slide 1: Actuators for Mechatronics Applications
BJ Furman
11MAR2014
https://www.jameco.com/Jameco/Products/ProdImag/1939589.jpg
http://www.newport.com/images/web900w-EN/images/11633.jpg?img_width=600&img_height=448
http://www.firgelli.com/Uploads/ID3IMAGE1300907739.jpg

## Slide 2: Outline
Learning objectives
Context for this module
Permanent magnet dc (PMDC) motor theory
Interfacing to PMDC motors
RC servos

## Slide 3: Learning objectives
Explain how a permanent magnet dc (PMDC) motor works
Explain how an RC servo works
Interface a dc motor and an RC servo to a microcontroller
Control the speed of a DC motor and the angular orientation of an RC servo

## Slide 4: Context for this module
System to Control
Sensor
Signal Conditioning
Controller (Hardware & Software)
Power Interface
Actuator
User Interface
Power Source
BJ Furman 22JAN2011
ME 106
ME 154
ME 157
ME 195
ME 120
ME 284
ME 106
ME 120
ME 30
ME 106
ME 190
ME 187
ME 110
ME 136
ME 154
ME 157
ME 182
ME 189
ME 195
ME 106
ME 120
ME 106
INTEGRATION
Mechatronics Concept Map
‘Muscle’

## Slide 5: PMDC theory
Brush
Commutation ring
Two fundamental phenomena occur
  Generation of torque (Lorentz force law)
    An electric charge moving in a magnetic field experiences a force
  Generation of back EMF (Faraday’s law of induction)
    A conductor moving in a magnetic field generates a voltage
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html
BJ Furman SJSU Mechanical and Aerospace Engineering ME 285
+

## Slide 6: PMDC theory - Torque
Torque (Lorentz force law)
    An electric charge moving in a magnetic field experiences a force
Brush
Commutation ring
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 7: PMDC theory – Back EMF
Generation of back EMF (Faraday’s law of induction)
    A conductor moving in a magnetic field generates a voltage at the negative rate of change of the magnetic flux through the circuit
Brush
Commutation ring
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 8: Simple DC motor
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html
Torque constant (Nm/A)
Back EMF constant (V/rad/s)
Brush
Commutation ring

## Slide 9: Commutation – torque increasing
Which way will the coil rotate?
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 10: Commutation – maximum torque
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 11: Commutation – torque decreasing
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 12: Commutation – zero torque
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 13: Commutation – torque increasing
http://www.animations.physics.unsw.edu.au/jw/electricmotors.html

## Slide 14: Permanent magnet DC (PMDC) motor
http://www.maxonmotor.ch/e-paper/blaetterkatalog/pdf/save/bk_25.pdf

## Slide 15: PMDC motor electrical model
Introduction to Mechatronics, Figure 22.7 p. 538.
Write KVL around the loop
Reflection
  What happens as the motor speed increases? (Assume Vs is constant)
    How does I change?
    How does the change in I affect torque? (remember, T=KTI)
  What happens when motor speed reaches its maximum value?
    What value will I be?
    What value of torque will be available?
  What happens when the motor speed is zero (locked rotor)?
    What value will I be?
    What value of torque will be available?

## Slide 16: PMDC motor speed-torque behavior
From KVL equation
Introduction to Mechatronics, Figure 22.8 p. 539.
Observations
  Intercepts with speed axis
    No-load speed
  Intercepts with torque axis
    Stall torque
  Slope of speed-torque line
    Speed regulation constant (speed-torque gradient)
When expressed in SI units, KT == KE

## Slide 17: Power and efficiency for a PMDC motor
Power
Efficiency
Introduction to Mechatronics, Figure 22.10 p. 544.

## Slide 18: Gearheads
http://www.maxonmotor.ch/e-paper/blaetterkatalog/pdf/save/bk_31.pdf

## Slide 19: Speed – Torque Curve for a PMDC Motor
Mabuchi FF-130RH-15210 3V DC motor

## Slide 20: Speed – Torque Curve for a PMDC Motor
Finding operating parameters when torque is known

## Slide 21: Speed – Torque Curve for a PMDC Motor
Finding operating parameters when current is known

## Slide 22: Speed – Torque Curve for a PMDC Motor
Finding operating parameters when speed is known

## Slide 23: Speed – Torque Curve for a PMDC Motor
Effect of changing supply voltage

## Slide 24: Speed – Torque Curve for a PMDC Motor
Effect of internal resistance for battery supplies

## Slide 25: Speed – Torque Curve for a PMDC Motor
Effect of changing type temperature

## Slide 26: Speed – Torque Curve for a PMDC Motor
Mabuchi FF-130RH-15210 3V DC motor
https://www.jameco.com/Jameco/Products/ProdDS/1939589.pdf

## Slide 27: Actuators for Mechatronics Applications, cont.
BJ Furman
15JUL2011 (for 19JUL2011)
https://www.jameco.com/Jameco/Products/ProdImag/1939589.jpg
http://www.newport.com/images/web900w-EN/images/11633.jpg?img_width=600&img_height=448
http://www.firgelli.com/Uploads/ID3IMAGE1300907739.jpg

## Slide 28: Outline
Additional actuators useful in mechatronics
Bi-directional control of PMDC motors
RC servos
RC servos interfacing to microcontrollers
Motor sizing

## Slide 29: Learning objectives
List additional actuators that are useful in mechatronic applications
Explain how an RC servo works
Interface a dc motor and an RC servo to a microcontroller
Control the speed of a DC motor and the angular orientation of an RC servo
Size a motor

## Slide 30: Brushless motors
Commutation is handled electronically, rather than mechanically
  Advantages
    No brushes to wear out
    High speeds possible (>100 kRPM)
    Low electrical noise
    Low rotor inertia (fast dynamics)
http://ww1.microchip.com/downloads/en/AppNotes/00885a.pdf
  Disadvantages
    More complicated to control
    Higher cost

## Slide 31: Linear motors
PMDC (brushless) and stepper varieties
  Direct drive for linear actuation
    No backlash from gearing or belt/pulley
  High accelerations
http://www.baldor.com/products/linear_motors.asp
Linear Stepper Motors:
Single and 2-axis

## Slide 32: Linear actuators
Combine a motor with a leadscrew
http://en.wikipedia.org/wiki/File:Linear_actuator_basic.gif
www.firgelliauto.com/

## Slide 33: Linear motion stage
Buy complete or build your own
http://www.thomsonlinear.com/

## Slide 34: Voice-coil actuator
High acceleration
Smooth motion
Need position feedback to know where you are
http://www.beikimco.com/actuators_linear_CYL.php
http://www.duxcw.com/digest/guides/hd/cheetah.gif

## Slide 35: Picomotor
Piezo-actuated micropositioning device
http://www.newport.com/
Cost ~$500 (driver not included)

## Slide 36: Picomotor actuating principle
Simple to drive – like a stepper motor (step and direction)
“Set and forget” operation
870x user manual Rev. C, p. 7.

## Slide 37: Other piezoelectric actuators
Large travel, flexure guided
  2000 micron travel, 160 N force
http://www.dynamic-structures.com/piezo.html
High precision, with capacitive position sensing
  Up to 38 micron travel, 1 nm position resolution
http://www.physikinstrumente.com/
Squiggle motor
  Small package, low force, self-locking
http://www.newscaletech.com/

## Slide 38: Many other actuators
Solenoids
Pneumatic actuators
  http://www.smcusa.com/smc.aspx
Hydraulic actuators
http://www.ledex.com/
http://www.hydraulicpumpsmotors.com/wp-content/uploads/2011/02/Hydraulic-Actuator.jpg

## Slide 39: Bidirectional control of motors
Introduction to Mechatronics, Figure 23.11 p. 562.
H-bridge – 4 transistors arranged in two ‘push-pull’ pairs
  Allows current to flow through the motor in either direction with a single-polarity power supply
‘Push-Pull’ pair
(totem pole)

## Slide 40: Bidirectional control of motors – LR current flow
H-bridge
  What are the diodes used for?
  Why a combination of NPN and PNP transistors?
  Need to be careful of ‘shoot-through’ current when switching directions
Introduction to Mechatronics, Figure 23.12 p. 562.

## Slide 41: Bidirectional control of motors – dynamic braking
Turning on only the upper transistors (or only the lower transistors) effectively shorts the motor terminals
  Voltage drop across a diode and a transistor dissipates energy faster than simple coast down
Introduction to Mechatronics, Figure 23.14 p. 564.

## Slide 42: H-bridge chips
SN754410NE
L293D
  Quad half-H (2 full H-bridges)
  Vcc2 can be 4.5 V to 36 V
  1 A max continuous per half-H
  Kickback diodes are built-in (but not L293B)
L298
  Dual, full-H (no diodes incl.)
  Vsupply can be 2.5 V to 46 V
  2 A max continuous per H
LMD18200
For higher currents
  TLE5206 (single H, 5 A continuous, Vsupply 6 V to 40 V)
  DVR8402 (dual H, 5 A per H can be paralleled, Vsupply 0 V to 50 V)
SN754410NE data sheet
L298 data sheet

## Slide 43: H-bridge design example
Design a bidirectional control interface using L293B for:
  Maxon RE-13 motor using a 12 V power supply
    Rterminal = 14.1 ohm
    L = 0.48 mH
    PWM frequency = 1 kHz
  Procedure:
    Check that L293B can handle Istall
    Choose kickback diodes (need trr < 200 ns and that can handle inductive transient current and power)
      If L293D were chosen, kickback diodes are built-in
      1N4935 has trr < 200 ns, 10 A peak intermittent, and 1 A max continuous Iforward with 1.2 V forward voltage drop  1.2 W
        Assume diodes dissipate all transient energy (conservative)
(= Vsupply/Rterminal = 12 V/14.1 ohm = 0.851 A, okay)
http://www.electromate.com/db_support/webphoto/MaxonRE.jpg

## Slide 44: H-bridge design example schematic
Bidirectional control for Maxon RE-13 motor using L293B
  Could avoid external diodes by using L293D
Introduction to Mechatronics, Figure 23.12 p. 562.

## Slide 45: Speed Control via PWM
Pulse-Width Modulation (PWM)
  Commonly used technique to control speed using digital output
  Basic idea:
    Switch power (applied voltage) to the motor on and off fast enough, so that the effect of switching is negligible
    The resulting average voltage == fraction of time the voltage is on
      Duty cycle (%) == “On time”/Period x 100%
    See PWM_demo.vi
  Choose period (1/freq) to be high enough that torque (and current) ripple can be tolerated
    10x shorter than the motor time constant, which is usually on the order of msec, so maybe 20 kHz

## Slide 46: RC (radio controlled) Servo
http://www.servocity.com/html/s3003_servo_standard.html
Incorporates a PMDC motor, gearing, and control electronics
http://www.pyroelectro.com/tutorials/servo_motor/servomotor.html
Model airplanes, cars, toys, and more!
Simple, low cost
Controlled by PWM signal (0-5 V)
  Pulse duration determines shaft angle
    0.5< t <3 ms pulse
    20 – 30 ms period
Introduction to Mechatronics, Figure 27.19 p. 637.
(or white)
~1.5 ms is ‘centered’
Futaba S3003 standard servo

## Slide 47: RC servo control system
Averaged PWM signal is compared to pot voltage
  Controller moves the motor to eliminate the error
  Can ‘hack’ for continuous rotation (PWM for speed control)
    See http://www.seattlerobotics.org/guide/servohack.html
Pot
http://mbed.org/cookbook/Servo
http://www-cdr.stanford.edu/dynamic/servo/
http://www.princeton.edu/~mae412/TEXT/NTRAK2002/292-302.pdf

## Slide 48: RC Servo resources
  http://mbed.org/cookbook/Servo
www.servocity.com
http://www.princeton.edu/~mae412/TEXT/NTRAK2002/292-302.pdf
http://pcbheaven.com/wikipages/How_RC_Servos_Works/
http://www.seattlerobotics.org/guide/servohack.html (modification for continuous rotation)

## Slide 49: Sizing a motor – guiding ideas
Peak Torque, Tpeak
Effective Continuous Torque (RMS Torque), TRMS
Maximum Speed, max
Other Factors, e.g., size, weight, cost, etc.

## Slide 50: Sizing a motor - procedure
Make a ‘ballpark’ estimate of the power required using rough calculations, estimation, or measurements
  P = Torque x angular speed (rad/s) or F x velocity
    Torque = radius x F
Calculate, estimate, or measure Text, Tfric (Note: may need to make an estimated guess about any gearing that might be needed)
Calculate motion parameters (angular speed and acceleration)
Calculate inertia parameters ‘reflected’ to the motor shaft
Calculate Tpeak
Compare to your ‘ballpark’ estimate for a sanity check
Look for a motor with 1.5Tpeak capability
Check max
Iterate based on choices
Check TRMS
Make sure that the motor can also deliver a continuous torque of TRMS or higher

## Slide 51: Sizing a motor - example
Refer to handouts
  Motor sizing example (hand written)
  Motor sizing example (Mathcad)
  Motion Control Mechanics
Outline of the example
  Given information:
    Polar moment of inertia of load
    Friction torque
    Motion profile
    Supply voltage and current (5 A max at 24 V)
  Select a motor that will meet the requirements

## Slide 52: For More Information
Mabuchi Motor Technical Reference
      http://www.mabuchi-motor.co.jp/en_US/technic/index.html
DC Motor Tutorials from MicroMo
      http://www.micromo.com/dc-motor-tutorials.aspx
Maxon Motor Academy
      http://www.maxonmotor.com/maxon-academy.html
Maxon Motor e-Catalog
      http://www.maxonmotor.ch/e-paper/
RC Servo tutorial
      http://www.pyroelectro.com/category/tutorials/

## Slide 53: Stepping motors
Operating principle
Construction
Inherent characteristics
Features
Advantages/Disadvantages

## Slide 54: PM Stepper motor – simplified model
Rotor
  Rotatable magnetized disk
Stator
  Two windings (phases)
A1
B1
A2
B2
N
S

## Slide 55: Stepper Motor Operation - Full Step Mode 1a
Step 1a
  Energize windings
    A1 and B1 high
    A2 and B2 low
  What happens to the rotor?
A1
B1
A2
B2
N
S
N
S
low
high
low
high
N
S
N
S

## Slide 56: Stepper Motor Operation - Full Step Mode 1b
Step 1b
  Magnetic forces cause a torque
  Rotor aligns with stator field
A1
B1
A2
B2
N
S
N
S
low
high
low
high
N
S
N
S

## Slide 57: Stepper Motor Operation - Full Step Mode 2a
Step 2a
  Energize windings
    A2 and B1 high
    A1 and B2 low
  What happens to the rotor?
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 58: Stepper Motor Operation - Full Step Mode 2b
Step 2b
  Magnetic forces cause a torque
  Rotor aligns with stator field
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 59: Stepper Motor Operation - Full Step Mode 3a
Step 3a
  Energize windings
    A2 and B2 high
    A1 and B1 low
  What happens to the rotor?
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 60: Stepper Motor Operation - Full Step Mode 3b
Step 3b
  Magnetic forces cause a torque
  Rotor aligns with stator field
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 61: Stepper Motor Operation - Full Step Mode 4a
Step 4a
  Energize windings
    A1 and B2 high
    A2 and B1 low
  What happens to the rotor?
A1
B1
A2
B2
N
S
N
S
low
high
low
high
N
S
N
S

## Slide 62: Stepper Motor Operation - Full Step Mode 4b
Step 4b
  Magnetic forces cause a torque
  Rotor aligns with stator field
The process repeats…
  Back to energizing:
    A1 and B1 high
    A2 and B2 low
  And the rotor rotates to position 1b
A1
B1
A2
B2
N
S
N
S
low
high
low
high
N
S
N
S

## Slide 63: Stepper Motor Operation – Half Stepping
Initial state
  Energize windings
    A1 and B1 high
    A2 and B2 low
  Then, turn off the A winding
    What happens?
A1
B1
A2
B2
N
S
N
S
low
high
low
high
N
S
N
S

## Slide 64: Stepper Motor Operation – Half Stepping 1a
Step 1a
  Turn off A winding, leave B on
    B1 high
    A1, A2 and B2 low
  What happens?
A1
B1
A2
B2
N
S
low
low
low
high
N
S
N
S

## Slide 65: Stepper Motor Operation – Half Stepping 1b
Step 1b
  Resultant field rotates 45°
  Magnetic forces cause a torque
  Rotor aligns with stator field
    Now the rotor turns only 45 degrees, one half of a step!
A1
B1
A2
B2
N
S
low
low
low
high
N
S
N
S

## Slide 66: Stepper Motor Operation – Half Stepping 2a
Step 2a
  Energize windings
    A2 and B1 high
    A1 and B2 low
  What happens to the rotor?
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 67: Stepper Motor Operation – Half Stepping 2b
Step 2b
  Resultant field rotates 45°
  Magnetic forces cause a torque
  Rotor aligns with stator field
    Now the rotor turns only 45 degrees, one half of a step!
  Continue the pattern
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 68: Stepper Motor Operation – microstepping
Suppose partial energization of a winding?
  Say, reduce B winding voltage by 15%
    What happens?
A1
B1
A2
B2
N
S
N
S
high
low
low
high
N
S
N
S

## Slide 69: Variable Reluctance (VR) Stepper Motor
Rotor
  Just a magnetically permeable material, but with ‘teeth’
Teeth align to pole pieces depending on which winding is energized
Advantages
  Smaller steps
  Lower cost
Disadvantages
  No ‘holding’ torque without winding current
Introduction to Mechatronics, Figure 26.4, p. 603

## Slide 70: How torque is created
Torque is made in the air gap
FT
F
FN
STATOR
ROTOR
Slide courtesy of Nick Johantgen, Oriental Motors, Inc.
Notes: The rotor and the stator do not touch one another. Many people think that since the rotor and the stator appear to have “gear” teeth, they must mesh together as the motor turns. Let me assure you that this is not the case! The rotor and the stator are separated by a very thin air gap, somewhere in the neighborhood of 0.0008”.
Since the teeth do not mesh together, torque must be “made” in the air gap. And that torque is a function of the magnetic flux focused from the rotor to the stator. Flux can be broken down into two components, a tangential component labeled FT above and a normal component labeled FN above. It is only when the tangential component is present that we are making torque.
When the teeth are lined up directly across from one another, the magnetic flux is flowing directly across, i.e., we have only a normal component. Since no tangential component is present, we are producing no torque and are in a stable position. However, as the teeth start deflecting away from one another, the flux has a tangential component and torque is produced. The greater the tangential component, the greater the torque.

## Slide 71: Hybrid Stepper Motor
Combines features of PM and VR stepper designs
Rotor
  Toothed
  End caps are indexed ½ tooth pitch
  Magnetized north on one end, south on the other
http://www.shinano.com/motors/docs/SKC_stepper_operation.pd

## Slide 72: Hybrid Stepper Motor Operation
Typical
http://www.shinano.com/motors/docs/SKC_stepper_operation.pd

## Slide 73: Torque vs. displacement
1
2
3
4
Slide courtesy of Nick Johantgen, Oriental Motors, Inc.
Notes: Now, let me explain what happens when a single phase is energized. The flux is flowing across from tooth A to tooth B. We have no tangential component and therefore no torque. We are in a stable rest position as denoted by 1 in the curve. Now, as the teeth start to deflect from one another, we begin to get the tangential component. Torque is produced and we say it’s negative because the torque is trying to get us back to the last stable rest position.
The maximum torque is produced when the teeth are 1/4 of a tooth pitch apart. The majority of the flux is flowing across to tooth B. Beyond this point, we reach an unstable point labeled 3 in the curve. Half of the flux is flowing from A to B and half from A to C. It’s unstable because the motor could go back to the last stable position or forward to the next position.
Finally, we reach a positive maximum denoted 4 in the curve. The majority of the flux is now flowing to tooth C and the torque is pulling us to the next stable rest position.
So, what’s the significance of this?

## Slide 74: Two phase torque ripple
Slide courtesy of Nick Johantgen, Oriental Motors, Inc.
Notes: Each phase is contributing to the total torque/speed curve of the motor. But, the torque is not constant. As shown in the graph above, the torque is actually rising and falling (from peak to valley) between successive phases. The average torque would be somewhere in between.
As an example, let’s say we’re running our load at a constant speed of 60 RPM. The motor’s average torque may be 50 oz-in, but it is really varying from some maximum value, say 56 oz-in, and some minimum value, say 45 oz-in. This torque variation (ripple) will cause vibration of the load. The greater the torque ripple, the greater the vibration. The worst case torque ripple for two phase motors is 29% and that causes quite a bit of vibration as we will see later.

## Slide 75: Torque/Speed curve
Speed
(PPS)
Max Starting
Speed
Max Running
Speed
Pullout
Torque
Pull-In
Torque
Start/Stop
Region
Holding
Torque
Torque (oz-in)
Slide courtesy of Nick Johantgen, Oriental Motors, Inc.

## Slide 76: Stepper motor drive configurations
http://www.probotix.com/stepper_motors/unipolar_bipolar/
http://www.astrosyn.com/shopimages/technicalguides/Guide%20to%20Stepper%20Motor%20Drive%20Selection.pdf

## Slide 77: Stepper motor drivers
http://www.allmotion.com/EZInchdescription.htm

## Slide 78: Low-cost stepper motor drive
http://www.ti.com/lit/ds/symlink/sn754410.pdf
Uses the SN754410 Quad Half-H chip

## Slide 79: Features
Known, relatively accurate basic step angle
  7.2o, 3.6o, 1.8o, .9o, .72o, and 0.36o per step
    ± 0.05o accuracy
Non-cumulative error
  Basic accuracy applies regardless of number of steps
Very high repeatability
One pulse, one step
Output speed == pulse rate
Relatively fast response
  Low rotor inertia  high accelerations
Relatively high torque per volume
Brushless  high reliability

## Slide 80: Advantages/Disadvantages
See ‘Features’ list
Can position without a sensor
May be more cost effective than other approaches
Disadvantages
  Power dissipation
  Vibration (particularly 2-phase motors. 5-phase much better)
  Need to mind pull-in/pull-out torques
  Relatively low-speed operation