## Slide 1: Interfacing to Control Power
BJ Furman
03MAR2016
https://www.jameco.com/Jameco/Products/ProdImag/1939589.jpg
Introduction to Mechatronics, Figure 17.16, p. 410.
http://arduino.cc/en/uploads/Main/ArduinoDuemilanove.jpg

## Slide 2: What does this symbol represent?
http://upload.wikimedia.org/wikipedia/commons/thumb/a/a1/Check_Valve.svg/500px-Check_Valve.svg.png
http://www.clippard.com/downloads/PDF_Documents/Application_and_Training/Clippard%20Schematic%20symbols.pdf
Or
Check valve

## Slide 3: Outline
Learning objectives
Context for this module
Diodes
Bipolar junction transistors (BJT)
MOSFETs
Using transistors to control power

## Slide 4: Learning objectives
Explain the theory, construction, and behavior of a diode
Explain the theory, construction, and behavior of a bipolar junction transistor (BJT)
Explain the theory, construction, and behavior of a MOSFET
Design an interface between a microcontroller and device that needs significant power

## Slide 5: Context for this module
System to Control
Sensor
Signal Conditioning
Controller (Hardware & Software)
Power Interface
Actuator
User Interface
Power Source
BJ Furman 22JAN2011
ME 106
ME 154
ME 157
ME 195
ME 120
ME 284
ME 106
ME 120
ME 30
ME 106
ME 190
ME 187
ME 110
ME 136
ME 154
ME 157
ME 182
ME 189
ME 195
ME 106
ME 120
ME 106
INTEGRATION
Mechatronics Concept Map
‘Muscle’

## Slide 6: Diode Types and Circuit Symbols
Diode Types
  Signal Diodes
  Rectifier Diodes
  Transient Voltage Suppress (TVS) Diodes
  Light Emitting Diodes
  Zener Diodes
Anode (P)
Cathode (N)
Symbol:
Actual Device:
Anode (P)
Cathode (N)
Surface mount
http://www.ebay.com/itm/Dual-H-Bridge-DC-Stepper-Motor-Drive-Controller-Board-Module-L298N-for-arduino-/251080674810

## Slide 7: P-N Junction – Forward Bias
P Type
  Doped with Boron or Gallium (1 Less e-)
N Type
  Doped with Arsenic or Phosphorous (1 Extra e-)
Anode (P)
Cathode (N)
+ -
Holes
e-
Net current
A Diode
is formed by
A junction between positively and negatively doped semiconductor material
P N

## Slide 8: P-N Junction – Reverse Bias
P Type
  Doped with Boron or Gallium (1 Less e-)
N Type
  Doped with Arsenic or Phosphorous (1 Extra e-)
Anode (P)
Cathode (N)
- +
P N
Holes
e-
No net current

## Slide 9: I-V Characteristic for a Diode (non-linear)
V
I
Forward Bias
Anode voltage higher than cathode voltage
Reverse Bias
Cathode voltage higher than anode voltage
IV Characteristic for a Resistor
Breakdown Voltage 50-1000V
0.6 to 0.7 V for silicon diode,
For LED ~ 1.5 V (IR) – 3.8 V (Blue)
= 1/R
Why do you need a resistor in series with a diode?
Anode (P)
Cathode (N)

## Slide 10: I-V Characteristic for a Zener Diode
Anode (P)
Cathode (N)
Introduction to Mechatronics, Figure 10.8, p. 203.

## Slide 11: Diode Example 1
Find VD, IR, VR, R = 1Ω (assume Vf = 0.7 V, and look closely at the diagram)
+ VD -
+ VR -
IR
-
10V
+
VD = -10V, VR = 0, IR = 0

## Slide 12: Diode Example 2
Find VD, IR, VR , R = 1Ω (assume Vf = 0.7 V)
+ VD -
+ VR -
IR
+
10V
-
VD = 0.7V
VR = 10 – 0.7 = 9.3V
IR = 9.3 / 1 =9.3A

## Slide 13: Diode Applications
AC Rectification
  Half wave
+ VD -
+ VR -
IR
+
10V
-
~
  Full wave
http://newton.ex.ac.uk/teaching/CDHW/Electronics2/PHY2028-C14.2.gif
http://www.bowdenshobbycircuits.info/page12.htm#317.gif

## Slide 14: Bipolar Junction Transistor (BJT)
Construction and schematic
So, B-C and B-E junctions look like…?
  Remember this!
Introduction to Mechatronics, Figure 10.15, p. 206.
Notes: Look at the slices of semiconducting material (say for the NPN-type): between B and C – a P-N junction, and between B and E – a P-N junction. What is a P-N junction? A diode. You will get current flow from B to E if you forward bias (hold B at a voltage higher than E by about 0.7 volts).

## Slide 15: BJT Operation (conceptual)
Like a current-controlled valve where base-emitter current controls collector-emitter current
  Hydraulic analogy for NPN
  How much ‘pressure’ (i.e., voltage, VBE) is needed to cause iBE?
Introduction to Mechatronics, Figure 10.16 p. 206.
Introduction to Mechatronics, Figure 10.17 p. 207.
Key concepts
Must turn on B-E diode to get C-E current
Ic = hfeIB (up to saturation)
Notes: The flow of current from base to emitter enables a larger flow of current from collector to emitter. The condition where the Vbe is less than 0.7 V is called the ‘cut-off’ region. In this region, there is not enough pressure to open the BE ‘check valve’, so no BE current flows. Consequently, the CE ‘valve’ will be closed, and no Ice current will flow. If Vbe is large enough to get current flowing from B to E, then the CE ‘valve’ opens in proportion to the BE current, but only up to the point that the valve is fully opened. This region of operation is called, ‘the linear region’, because Ice = hfe*Ib (roughly). That is, Ice is approximately proportional (linear) to Ibe by a proportionality constant called hfe, the ‘dc current gain’. Now there comes a point where the CE valve is fully opened, and further increase in Ibe does not produce more Ice. This point is called saturation. When the transistor is saturated, the Ice will depend on the voltage urging Ic current, the Vce_sat, and whatever is restricting current flow from C to E. hfe is on the order of 30 to 1000 depending on the transistor

## Slide 16: BJT low-side drive
Introduction to Mechatronics, Figure 10.18 p. 207.
For mechatronics, transistors are mostly used as electronically controlled switches
  Either fully off (cut off) or fully on (saturated)
    Want to avoid the in-between condition (linear region). Why…?
      Minimize power dissipation in the transistor
Chart: Vce vs. Vin
| -3 | 0 | 0.3 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
 | 12 | 12 | 12 | 12 | 12 | 11.5 | 11 | 10.5 | 10 | 9.5 | 9 | 8.5 | 8 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2 | 1.5 | 1 | 0.5 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3 | 0.3
Chart: Ic vs. Vin
| -3 | 0 | 0.3 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4 | 23.4
Chart: Pt vs. Vin
| -3 | 0 | 0.3 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
 | 0 | 0 | 0 | 0 | 0 | 0.0115 | 0.022 | 0.0315 | 0.04 | 0.0475 | 0.054 | 0.0595 | 0.064 | 0.0675 | 0.07 | 0.0715 | 0.072 | 0.0715 | 0.07 | 0.0675 | 0.064 | 0.0595 | 0.054 | 0.0475 | 0.04 | 0.0315 | 0.022 | 0.0115 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702 | 0.00702
Chart: Pload vs. Vin
| -3 | 0 | 0.3 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008 | 2.5000000000000009 | 2.600000000000001 | 2.7000000000000011 | 2.8000000000000012 | 2.9000000000000012 | 3.0000000000000013 | 3.1000000000000014 | 3.2000000000000015 | 3.3000000000000016 | 3.4000000000000017 | 3.5000000000000018 | 3.6000000000000019 | 3.700000000000002 | 3.800000000000002 | 3.9000000000000021 | 4.0000000000000018 | 4.1000000000000014 | 4.2000000000000011 | 4.3000000000000007 | 4.4000000000000004 | 4.5 | 4.5999999999999996 | 4.6999999999999993 | 4.7999999999999989 | 4.8999999999999986 | 4.9999999999999982
 | 0 | 0 | 0 | 0 | 0 | 0.0005 | 0.002 | 0.0045 | 0.008 | 0.0125 | 0.018 | 0.0245 | 0.032 | 0.0405 | 0.05 | 0.0605 | 0.072 | 0.0845 | 0.098 | 0.1125 | 0.128 | 0.1445 | 0.162 | 0.1805 | 0.2 | 0.2205 | 0.242 | 0.2645 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378 | 0.27378
Consider
hfe= 100 (current gain)
V+= 12 V
Vce(sat)= 0.3 V
RB= 10 kohms
Rload=500 ohms
Plot Vce, Ic, Pt, and Pload vs. Vin

## Slide 17: BJT low-side drive example
Introduction to Mechatronics, Figure 10.18 p. 207.
Find RB to turn on the lamp (Rload)
  Rload= 100 ohms
  Vce(sat)= 0.3 V
  V+= 10 V
  Vin = 5.0 V
Procedure
Work backward starting with the load. Find a candidate transistor that can handle the required ICE current and VCE voltage.
  What Ic is needed for saturation?
  Find a transistor that will handle Ic and V+ (data sheet)
  Determine hfe and Vce(sat) at Ic(sat) from the data sheet
  Determine iB(minimum) to saturate the transistor:
  Select RB to give iB with some extra margin (2x – 10x):
Notes: Make this an exercise.
We usually know what voltage and current the load needs. A quick estimate of the maximum current that could be delivered to the load can be found by applying Ohm’s law across the load V/Rload. To be more accurate, once we select a candidate transistor, we can find VCE_sat from the data sheet and use it to find Ic_sat, then work backward from the point of saturation to determine the base current, and then the base resistor value to insure that the transistor will always be driven into saturation.

## Slide 18: Review – Interfacing to Control Power
BJT (NPN and PNP)
  Current-controlled ‘switch’
    Controlled by base-emitter current
    Base emitter junction acts like a diode
      For NPN, need VBE > 0.6-0.7 V to get base-emitter current
  ic = hfe*ib up to saturation
  For our purposes, use BJT either cut-off or saturated
  Work backward from the saturation current
    Choose a BJT that can handle the current and voltage
    Determine the size of the base resistor, so that the microcontroller can drive the BJT into saturation
      Include some margin to guarantee saturation

## Slide 19: Example – Arduino to AC motor
Design an interface between the Arduino and a motor that requires 120 VAC, 2A

## Slide 20: Design the interface to the relay coil
How much current is needed?

## Slide 21: Configure the components

## Slide 22: Calculations – Follow the procedure
What current is needed to operate the relay?
  Coil voltage/coil resistance
What kind/size transistor is needed?
  Max. continuous current
  Max collector voltage
  hfe
What should Rb be?
  Choose to make sure that transistor is driven into saturation
    ib should be 2x – 10x what is needed to saturate
  Make sure that Arduino can supply the current
Add transient current protection (what is that?)
Notes: Data sheet for the relay said that Rcoil = 32 ohm, which, if driven at 5 V will need 5V/32 ohm = 0.156 A
Max collector voltage will be 5 V
hfe min =

## Slide 23: Configure the components

## Slide 24: Possible choice of transistor
2N3904
  See the data sheet
2N2222
  See the data sheet
ULN2803D
  See the data sheet
Final design
Prelim design

## Slide 25: The Darlington pair
Introduction to Mechatronics, Figure 10.24 p. 211.
Provides higher current gain
  For NPN VBE will be about 1.2 V
  Current gains in saturation are about 200 to 500:1
Popular versions
  TIP100 series
    TIP120
  ULN2803 Octal driver
ST TIP120 data sheet
Motorola ULN2803 data sheet
Notes: Make this an exercise.

## Slide 26: Switching loads with having appreciable inductance
You must protect the transistor switch from transient voltages when driving inductive loads
  Motors, solenoids, etc. have relatively large inductance
    Inductance is analogous to…?
      Inertia
  Problem arises when turning the switch off
    Collapsing magnetic field will create a transient voltage spike
      Ex. L=200 mH, 0.65 A, 1ms switching time
  Need a way to dissipate the energy
    Use a diode (at the very least)
    Diode plus Zener diode or TVS diode better
BIG Problem!
Introduction to Mechatronics, Figure 23.1 p. 553.
Introduction to Mechatronics, Figure 23.4 p. 553.

## Slide 27: Choosing the transient suppression components
Simple diode
  Fast recovery time, trr
    A few hundred nanoseconds or less
    Ex. 1N4933
  Select diode so that its peak intermittent current is greater than the maximum current you need to switch off
Simple diode plus Zener diode
  Choose the Zener so that its reverse-breakdown voltage does not exceed the VCE or VDS maximum of the transistor and that it can handle the maximum current that will be switched off
TVS diodes
  http://www.littelfuse.com/data/en/Product_Catalogs/Littelfuse_TVS_Diode_Catalog.pdf
Introduction to Mechatronics, Figure 23.7 p. 558.
Introduction to Mechatronics, Figure 23.4 p. 553.

## Slide 28: The interface design
Back

## Slide 29: Interface with ULN2803

## Slide 30: BJT high-side drive
If load must be referenced to ground
Uses a PNP transistor
  Turn on by making Vin at least 0.6 V lower than +10 V
  Turn off by making Vin at least +10 V - 0.6 V
Introduction to Mechatronics, Figure 10.23 p. 210.
Would this work with the Arduino?
Notes: Make this an exercise.
Use an NPN transistor with its collector tied (through a current limiting resistor) to 10 V and to Vin. To turn on the lamp, write HIGH to the pin connected (through a current limiting resistor) to the base of the NPN transistor.

## Slide 31: The MOSFET
Introduction to Mechatronics, Figure 10.27 p. 213.
Metal Oxide Semiconductor Field Effect Transistor
  Distinctions from BJT
    Voltage controlled, rather than current controlled as for the BJT
    Conduction path (D-S) behaves like a small resistance rather than a fixed voltage drop when fully on
    Enhancement and depletion types
  Gate-source voltage controls drain-source current
    N-channel (enhancement) fully turns on when VGS > VOn
      VOn = 4.5 V for logic-level types, 10 V for non-logic level types
    P-channel (enhancement) turns on when VSG > VOn
    RDS drops to a relatively low value when device is fully on
      mOhms for power MOSFETs
Introduction to Mechatronics, Figure 10.28 p. 213.
Notes: Make this an exercise.

## Slide 32: The MOSFET (hydraulic analogy)
Introduction to Mechatronics, Figure 10.29 p. 213.
Gate to source ‘pressure’ (voltage) controls drain-source flow restriction (RDS)
  Small gate capacitance
    Small transient current to build up VGS, but none needed in steady state
Notes: Make this an exercise.

## Slide 33: MOSFET high and low-side drive examples
Introduction to Mechatronics, Figure 10.32 p. 215.
Low-side drive
  Use an N-channel MOSFET
    For ‘logic level’ MOSFET, VGS should be about 5 V to achieve low RDSon
    For regular power MOSFET, VGS should be about 10 V to achieve low RDSon
High-side drive
  Use a P-channel MOSFET
    For ‘logic level’ MOSFET, VGS should be about -5 V to achieve low RDSon
    For regular power MOSFET, VGS should be about -10 V to achieve low RDSon
Introduction to Mechatronics, Figure 10.33 p. 216.
Low-side drive
High-side drive
Notes: Make this an exercise.

## Slide 34: Logic Level vs. ‘regular’ Power MOSFET
http://www.vishay.com/
IRL520
IRF520

## Slide 35: BJT vs. MOSFET – which to use?
Depends on how much control voltage and current is available
  Some overlap where either type could be used
    Decide based on cost, complexity, and efficiency
  BJT advantages
    When control voltage is relatively small (i.e., less than 3 V)
    Higher voltage switching capability
  MOSFET advantages
    When lowest voltage drop or lowest power dissipation across the switch is required
    When sufficient voltage is available, but not sufficient control current
      Gate drivers are available (ex. LTC1157)
    Less complex (no extra resistor), but may be more expensive

## Slide 36: Intrinsically Safe Circuits
http://www.omega.com/temperature/z/pdf/z131-148.pdf

## Slide 37: For More Information
Transient Suppression Devices and Principles
      http://www.littelfuse.com/data/en/Application_Notes/an9768.pdf
The application of relay coil suppression with DC relays
      http://relays.te.com/appnotes/app_pdfs/13c3311.pdf
Coil Suppression Can Reduce Relay Life
      http://relays.te.com/appnotes/app_pdfs/13c3264.pdf
Determining Relay Coil Inductance
      http://relays.te.com/appnotes/app_pdfs/13c3344.pdf

## Slide 38: Review from last lecture
BJT used as an ‘electronic switch’ to control power
Two ‘flavors’ of BJT
  NPN
    Turn on with Vbe > 0.6 V
    Ice is controlled by ibe up to saturation
    Up to saturation, ic = hfe*ib
    Make sure that transistor IS driven into saturation
  PNP
    Turn on with Veb > 0.6 V
    Currents flow oppositely to NPN