## Slide 1: Lecture 12: Spreadsheets for Engineering Applications - part 2
BJ Furman
14NOV2011

## Slide 2: The Plan for Today
Solver
  Review
  Non-linear regression analysis
Aerospace engineering computation using a spreadsheet
Macros and VBA programming

## Slide 3: Learning Objectives
Use Solver to solve mathematical equations
Apply Solver to perform regression (linear and non-linear)
Explain the utility of Visual Basic for Applications (VBA)
Create a VBA macro to automate tasks

## Slide 4: Excel Solver
Add-in tool comprised of optimization algorithms
  Goal: minimize or maximize an objective function subject to constraints by changing a set of parameters that the objective function depends upon
Can be used to find roots, solve simultaneous equations, solve problems requiring iteration, etc.

## Slide 5: Activating Solver - Excel 2003
Make sure Solver Add-in is checked!

## Slide 6: Activating Solver - Excel 2007
Office Button

## Slide 7: Solving Simultaneous Equations
Circuit analysis (EE 98)
  Find the currents
Kirchhoff’s Current Law at A
Kirchhoff’s Voltage Law across R1 and R3
R2
R1
R3
+V
i1
i2
i3
A
Equations in matrix form
Could solve by matrix inversion: [ i ] = [A]-1[V], but let’s use the Solver instead.

## Slide 8: Steps for Solving Simultaneous Equations With Solver
Steps
  Define constants and variables. Put guesses in for the variables.
  Express m equations in n variables (and constants) as: fi (xj)= 0, where i =1 to m, and j = 1 to n
  Form the equation: y = ∑ fi2
  Use the Solver, and change the xj values to drive y (the Target Cell) to be zero
Example: Excel_pt2.xls

## Slide 9: Circuit Analysis Example with Solver
1. Define constants and variables. Add guesses for variables
2. Express equations in the variables and constants
3. Form the equations: y = ∑ fi2
4. Solver, and change the variables to drive y (the Target Cell) to 0
Note: named ranges
On to Regression Analysis 

## Slide 10: Adding Names to Ranges
Highlight names and values
2003: Insert / Name / Create / Left column
2007: Formulas / Defined Names tab / Create from Selection / Left column
Result
Back

## Slide 11: Regression Analysis
Coined by biologist Francis Galton (1822-1911)
  Searching for a mathematical law describing the tendency of offspring’s characteristics to revert (regress) back to the average of ancestors its ancestors
Statistical method to investigate the relationship between dependent and independent variables
  Fit a mathematical model to a set of data
    Ex. “best-fit” straight line (trendline) through data points from a phenomena that is thought to be of the form: y=mx + b
  Find the coefficients of the model equation that minimizes the sum-of-squared error (SSE) between the actual dependent variable values and those predicted by the model

## Slide 12: Linear Regression
Linear regression
  Where the coefficients of the model are linear
Examples
y = mx + b
y = a + b log(x)
y = a + bX + cX2
error

## Slide 13: Non-linear Regression
Non-linear regression
  Where the coefficients of the model are non-linear
Example
y = Ae-t/t + C
error
Which coefficient is “non-linear”?

## Slide 14: Regression Analysis Procedure
Steps
  Select a regression model (e.g., y=mx+b)
  Enter the data set (dependent and independent variable values) and initial guesses for the regression model coefficients
  Calculate the predicted dependent values using the regression model and the independent variable(s)
  Calculate the 'error' values (actual-predicted)
  Calculate the squared errors
  Calculate the sum of the squared errors (SSE)
  Use Solver to minimize the SSE (the Target Cell, and select 'Min') by changing the value of the coefficients (m and b)
  Test your result by: 1) calculating the coefficient of determination (R2), 2) plotting your model curve to the data, 3) plotting Ypred vs. Yi, and 4) plotting the deviations (Yi - Ypred).
Notes: Guesses: m = 0.5 and b = 0
See the example spreadsheet

## Slide 15: Non-linear Regression Example
Thermal step response
  Expose an object at uniform temperature to a step change in surrounding temperature
    Ex: Lobster put into a pot of boiling water
      thermocouple at the center of the lobster
      measure lobster temperature as function of time
  Use the data to determine parameters of a first order model:
Assumed Solution
Example: Excel_pt2.xls

## Slide 16: Spreadsheet for Non-linear Regression
Example: Excel_pt2.xls
Model curve

## Slide 17: Plot of Ypred vs Yi
A good fit:
Data close to the diagonal line, Yi vs. Yi
(but will depend on scatter in the data)
No discernable pattern in the data points around the diagonal axis
Yi vs. Yi

## Slide 18: Deviation Plot
A good fit:
Yi-Ypred small
(but will depend on scatter in the data)
No discernable pattern in the data points around the horizontal axis

## Slide 19: Excel, Macros, and VBA
Macro: a set of recorded key strokes or program written in Visual Basic (VB) to automate tasks
Visual Basic for Applications (VBA)
  An implementation of VB integrated into MS Office applications
    Enables user to write VB code to automate tasks and much more.

## Slide 20: Security and Working With Macros
Be careful with macro enabled files!
  Excel 2007
    .xlsx - macro dis-abled workbooks (default)
    .xlsm - macro enabled workbooks
    You can write and work with a macro in a .xlsx file, but you can only save the macro to a .xlsm file.
    You may need to modify Macro Settings
      Office button | Excel Options | Trust Center Settings | Macro Settings | Disable all macros with notification
  Excel 2003
    Set security level to ‘medium’

## Slide 21: Accessing Macros in Excel 2003
Tools / Macro

## Slide 22: Accessing Macros in Excel 2007
View / Macro

## Slide 23: Recording Macros
Excel 2007
  View / Macros / Macros (menu) / Record Macro
Excel 2003
  Tools / Macro / Record New Macro
Ex. lbf to N conversion

## Slide 24: lbf to N Conversion Macro

## Slide 25: VB Editor

## Slide 26: Review

## Slide 27: References
Larsen, R. W. (2009). Engineering with Excel, Pearson Prentice Hall, New Jersey. ISBN 0-13-601775-4
Engineering with Excel companion website: http://www.chbe.montana.edu/excel/EngExcel3.htm. Visited 25OCT2009.
First-Order System: Transient Response of a Thermocouple to a Step Temperature Change. [Available on-line]. http://www.colorado.edu/MCEN/Measlab/background1storder.pdf. Visted 24APR2010.