## Slide 1: EE130 Electromechanics 2013
J. Arthur Wagner, Ph.D.
Prof. Emeritus in EE
wagneretal@sbcglobal.net

## Slide 2: Fig. 4.1 Voltage-link system
Vd is the voltage-link, or dc-bus voltage. Vd “sits” between two AC systems.
Vd does not reverse
because transistors can
block voltage with
only one polarity.

## Slide 3: Questions
Does the voltage link reverse in polarity?
Why?

## Slide 4: Fig. 4.2 Switch mode converters
Discuss figures and switching
e.g. Sw a up – down – up – down …. and sw b down only
e.g. Sw a up – down – up – down … sw b and sw c down only
PPU efficiency about 95 %

## Slide 5: Questions
How do you define PPU efficiency?
What is a typical value for PPU efficiency?

## Slide 6: Allegro stepper motor driver
Trace power pole for one phase

## Slide 7: Prototype board
Driver chip
12 V power supply = bus voltage
capacitor
note large traces

## Slide 8: Fig. 4.3 Switching power-pole
The switch contacts up and contacts down.
Never “open” or “floating”.
qa is a logic signal.
The inductance keeps the current flowing (with some ripple).

## Slide 9: Questions
What keeps the current flowing?

## Slide 10: Fig. 4.4 PWM of the switching pole
The logic signal is up = 1 and down = 0.
The period Ts is fixed. Tup varies, i.e. the Pulse Width is Modulated (PWM)
Note ida stops, i.e. goes to zero, ia continues.

## Slide 11: Question
Suppose Ts = 0.1 ms and Tup = 0.08 ms while Vd is
applied to the load.
What is the average voltage va?

## Slide 12: Average voltage, and “turns ratio”

## Slide 13: Homework Solutions 1-1

## Slide 14: Homework Solutions 2-11

## Slide 15: Homework Solutions 2-12

## Slide 16: Homework Solutions 2-13

## Slide 17: Homework Solutions 2-14

## Slide 18: Fig. 4.5 Bi-directional power flow
a FET sets a current direction, diode continues the flow.
q turns one FET ON, and other FET OFF
a bemf in the motor “bucks” (is against) Vd
current flows into Vd and “boosts” its voltage

## Slide 19: Question
Name a situation where the boost function is used.

## Slide 20: Fig. 4.6 Bidirectional switching power pole
The left FET and diode operate together when the current is
flowing out.
Question: Tell me how the right diode and FET operate together.

## Slide 21: Fig. 4.7 Switching-cycle average
Now .
always flows and
stops flowing
This transformer steps down the voltage and steps up the current.

## Slide 22: Question
Explain this statement:
always flows and
stops flowing

## Slide 23: Fig. 4.8 PWM Waveforms in a switching power pole
When vtri < vcntrl,a we have an UP, otherwise a DOWN.
Point out 1 cycle and one ½ cycle.

## Slide 24: Question
How does vcntrl,a vary with respect to vtri?

## Slide 25: Fig. 4.9 Switching power-pole and its duty-ratio control
We add onto the drawing the model which generates the switching signal qa
(Incidentally, we show variables as time functions.)

## Slide 26: Question
With respect to vcntrl,a and vtri,
when is qa UP and when is qa DOWN?

## Slide 27: Homework Chapter 4, Due next Tuesday
Problems 4.1, 4.2, 4.3, 4.4